## Slide 1: E-Bus Activities and Smart energy services for e-mobility Oslo 13.2.2017 Tammo Voigt

## Slide 2: The trend to Mega - Urbanisation is driving the demand for emmisionfree Public transport dramatically
53% of world population live in cities.
Today ca. 360 Million people are living in 23 megacities.
By 2025 more than 630 Million people will live in 37 megacities.
Notes: As of today already more than half of the world's population live in urban areas.
And urbanization is progressing: in 2050, the share of urban residents will be more than two third.
By 2050, the three megacities of New York, Delhi and Tokyo alone will have to buy more than 40,000 additional buses to be able to transport their citizens.
For years, transport operators have reported growing passenger numbers.
Last year, German transport operators counted more than ten billion passengers in buses and trains for the first time.

## Slide 3: Daimler Buses focusing on TCO optimized vehicles and on emission free driving for city bus application
Benchmark TCO & fuel economy Euro VI products
Continuous CO2 optimization
Downsizing
Compact Hybrid
Eco Steering (EHPS)
Zero emission driving for city traffic
E-Mobility Platform Citaro
E-Cell & F-Cell vehicles
Only partly emission free driving possible < 30km
Full-size Plug-in Hybrid
* TCO = Total Cost of Ownership


Nearly Emission Free
Emission Free
Partly Emission Free


## Slide 4: Our requirements regarding maturity level of a marketable product are not yet reached!
 | 0% |  |  |  |  | 50% |  |  |  |  |  | 100%
E-drive system |  |  |  |  |  |  |  |  |  |  |  | 
modular battery system |  |  |  |  |  |  |  |  |  |  |  | 
HVAC & thermomanagement |  |  |  |  |  |  |  |  |  |  |  | 
efficient steering system |  |  |  |  |  |  |  |  |  |  |  | 
energy management |  |  |  |  |  |  |  |  |  |  |  | 
system integration |  |  |  |  |  |  |  |  |  |  |  | 
electrical charging system |  |  |  |  |  |  |  |  |  |  |  | 
Development status 2016 Citaro E-Cell
2018
series production readiness

## Slide 5: Current perception shows large potentials to raise energy content of batteries with equal assembly space until 2030
module strategy 51Ah cell
potential
module strategy 37Ah cell
2015 2020 2025 2030
180%
160%
140%
120%
100%
energy content with equal assembly space

## Slide 6: Daimler Buses battery strategy will benefit from the Daimler modules
Passenger cars
  Each vehicle project with a specified battery
  Volume-optimized approach
Buses
  Derivation of a module strategy (1-16 sub-units)
  Highest scalability (150 – 400 kWh)
supplier
Mercedes-Benz Cars
Daimler Buses

## Slide 7: Outlook 2025: Battery development will significantly enhance the operation range for a city bus with depot-charging!
100% of all city bus operations
- 25°
+ 40°
range without recharging in operation
outside temperatures
- 20°
20°
10°
30°
comfort restrictions
300 km
- 10°
reach Citaro E-CELL without recharging in operation
F-Cell ?
Notes: Reichweite mit heute bekannten Techn lösungen

## Slide 8: Citaro E-Cell will be different than existing battery buses …
System Consulting Electromobility
optimised thermo- & energy management
modular battery
system
validated & tested system integration

## Slide 9: Daimler Buses developed a multi-level approach to initiate solutions
Data Acquisition & Analysis
System lay-out
Proof of concept
“roll-out” scenario
depot & fleet structure - operating distances - load profiles - vehicle cluster - …
vehicle & infrastructure spec. - charging power - battery size - heating concept - …
simulation & validation - energy consumption - charging scenarios - TCO - …
Fleet structure - Ramp-up scenario

## Slide 10: Modular system of energy services allows solutions tailored to customer needs
E-Bus/Van/Truck
Infrastructure
Energy/ V2G
Value-added services
Renewables
Infrastructure at depot: Charging stations and grid extension.
Optional stationary battery.
Cost optimization of electricity bill (energy cost, demand charges).
Additional revenues through Vehicle2Grid.
Option to obtain energy from renewable resources.
Full - service leasing
Sale
Pay per use
Prerequisite: Purchase of a Daimler e-vehicle.
Payment options
Consulting
Software support
Optimized TCO due to intelligent concept and operation
TCO simulation

## Slide 11: A tailored infrastructure solution for on-site charging including energy storage will be provided to the customer.
Required hardware
Legal and risk managers
On site charging
hardware
Grid extension
Installation service
Stationary battery
Connection of battery, charging pole to the grid
Required services
Software & IT services
Groundwork
Construction management
Architecture
On-site infrastructure
E-Bus on-site infrastructure

## Slide 12: Thank you for your Attention